## Slide 1: Packet switching

## Slide 2: Oultine
Switching and Forwarding
Bridges and LAN Switches
Cell Switches (ATM)

## Slide 3: Switching and Forwarding

## Slide 4: Switch
A mechanism that allows us to interconnect links to form a large network
A multi-input, multi-output device which transfer packets from an input to one or more outputs

## Slide 5: Switching and Forwarding
Adds the star topology to the point-to-point link, bus(Ethernet), and ring (802.5 and FDDI) topologies

## Slide 6: Properties of Star Topology
  A switch has a fixed number of inputs and outputs
    which limits the number of hosts that can be connected to a single switch
Large networks can be build by interconnecting a number of switches
We can connect switches to each other and to hosts using point-to-point links
  which typically means that we can build network of large geographic scope
Adding a new host to the network by connecting it to a switch does not necessarily mean that the hosts already connected will get worse performance from the network

## Slide 7: Switching and Forwarding
It is impossible for two hosts on the same Ethernet to transmit continuously at 10Mbps because they share the same transmission medium
Every host on a switched network has its own link to the switch
  So it may be entirely possible for many hosts to transmit at the full link speed (Bandwidth) provided that the switch is designed with enough aggregate capacity

## Slide 8: Switching and Forwarding
A switch is connected to a set of links and for each of these links, runs the appropriate data link protocol to communicate with that node
A switch’s primary job is to receive incoming packets on one of its links and to transmit them on some other link
  This function is referred as switching and forwarding
  According to OSI architecture this is the main function of the network layer

## Slide 9: Switching and Forwarding
How does the switch decide which output port to place each packet on?
  It looks at the header of the packet for an identifier that it uses to make the decision
  Two common approaches
    Datagram or Connectionless approach
    Virtual circuit or Connection-oriented approach
  A third approach source routing is less common

## Slide 10: Switching and Forwarding
Assumptions
  Each host has a globally unique address
  There is some way to identify the input and output ports of each switch
    We can use numbers
    We can use names

## Slide 11: Switching and Forwarding
Datagrams
  Key Idea
    Every packet contains enough information to enable any switch to decide how to get it to destination
      Every packet contains the complete destination address

## Slide 12: Switching and Forwarding
An example network
To decide how to forward a packet, a switch consults a forwarding table (sometimes called a routing table)

## Slide 13: Switching and Forwarding
Destination Port
-------------------------------------
A 3
B 0
C 3
D 3
E 2
F 1
G 0
H 0
Forwarding Table for Switch 2

## Slide 14: Characteristics of Connectionless (datagram) Network
A host can send a packet anywhere at any time, since any packet that turns up at the switch can be immediately forwarded (assuming a correctly populated forwarding table)
When a host send a packet, it has no way of knowing if the network is capable of delivering it or if the destination host even up and running
Each packet is forwarded independently of previous packets that might have been sent to the same destination
  Thus two successive packets from host A to host B may follow completely different paths
A switch or link failure might not have any serious effect on communication if it is possible to find an alternate route around the failure and update the forwarding table accordingly.

## Slide 15: Switching and Forwarding
Virtual Circuit Switching
  Widely used technique for packet switching
  Uses the concept of Virtual circuit (VC)
  Also called a connection oriented model
  First set up a virtual connection from the source host to the destination host and then send the data

## Slide 16: Switching and Forwarding
Host A wants to send packets to host B

## Slide 17: Switching and Forwarding
Two- stage process
  Connection setup
  Data Transfer
Connection Setup
  Establish “connection state” in each of the switches between the source and destination hosts
  The connection state for a single connection consists of an entry in the “VC table” in each switch through which the connection passes

## Slide 18: Switching and Forwarding
One entry in the VC table on a single switch contains
  A virtual circuit identifier (VCI) that uniquely identifies the connection at this switch and that will be carried inside the header of the packets that belong to this connection
  An incoming interface on which packets for this VC arrive at the switch
  An outgoing interface in which packets for this VC leave this switch
  A potentially different VCI that will be used for outgoing packets

## Slide 19: Switching and Forwarding
The semantics for one such entry is
  If a packet arrives on the designated incoming interface and that packet contains the designated VCI value in its header, then the packet should be sent out the specified outgoing interface with the specified outgoing VCI value first having been placed in its header

## Slide 20: Switching and Forwarding
Note:
  The combination of the VCI of the packets as they are received at the switch and the interface on which they are received uniquely identifies the virtual connection
  There may be many virtual connections established in the switch at one time
  Incoming and outgoing VCI values are not generally the same
    VCI is not a globally significant identifier for the connection; rather it has significance only on a given link
  Whenever a new connection is created, we need to assign a new VCI for that connection on each link that the connection will traverse
    We also need to ensure that the chosen VCI on a given link is not currently in use on that link by some existing connection

## Slide 21: Switching and Forwarding
Two broad classes of approach to establish connection state
  Network Administrator will configure the state
    The virtual circuit is permanent (PVC)
    The network administrator can delete this
    Can be thought of as a long-lived or administratively configured VC
  A host can send message into the network to cause the state to be established
    This is referred as signalling and the resulting virtual circuit is said to be switched (SVC)
    A host may set up and delete such a VC dynamically without the involvement of a network administrator

## Slide 22: Switching and Forwarding
Let’s assume that a network administrator wants to manually create a new virtual connection from host A to host B
  First the administrator identifies a path through the network from A to B
5
11
7
4

## Slide 23: Switching and Forwarding
The administrator then picks a VCI value that is currently unused on each link for the connection
  For our example:
    Suppose the VCI value 5 is chosen for the link from host A to switch 1
    11 is chosen for the link from switch 1 to switch 2
    So the switch 1 will have an entry in the VC table
Incoming Interface | Incoming VC | Outgoing Interface | Outgoing VC
2 | 5 | 1 | 11

## Slide 24: Switching and Forwarding
Similarly, suppose
  VCI of 7 is chosen to identify this connection on the link from switch 2 to switch 3
  VCI of 4 is chosen for the link from switch 3 to host B
  Switches 2 and 3 are configured with the following VC tables
Incoming Interface | Incoming VC | Outgoing Interface | Outgoing VC
3 | 11 | 2 | 7
Incoming Interface | Incoming VC | Outgoing Interface | Outgoing VC
0 | 7 | 1 | 4

## Slide 25: Switching and Forwarding
For any packet that A wants to send to B, A puts the VCI value 5 in the header of the packet and sends it to switch 1
Switch 1 receives any such packet on interface 2, and it uses the combination of the interface and the VCI in the packet header to find the appropriate VC table entry.
The table entry on switch 1 tells the switch to forward the packet out of interface 1 and to put the VCI value 11 in the header

## Slide 26: Switching and Forwarding
Packet will arrive at switch 2 on interface 3 bearing VCI 11
Switch 2 looks up interface 3 and VCI 11 in its VC table and sends the packet on to switch 3 after updating the VCI value appropriately
This process continues until it arrives at host B with the VCI value of 4 in the packet
To host B, this identifies the packet as having come from host A

## Slide 27: Switching and Forwarding
In real networks of reasonable size, the burden of configuring VC tables correctly in a large number of switches would quickly become excessive
  Thus, some sort of signalling is almost always used, even when setting up “permanent” VCs
  In case of PVCs, signalling is initiated by the network administrator
  Switched Virtual Circuits (SVCs) are usually set up using signalling by one of the hosts

## Slide 28: Switching and Forwarding
How does the signalling work
  To start the signalling process, host A sends a setup message into the network (i.e. to switch 1)
    The setup message contains (among other things) the complete destination address of B.
    The setup message needs to get all the way to B to create the necessary connection state in every switch along the way
    It is like sending a datagram to B where every switch knows which output to send the setup message so that it eventually reaches B
    Assume that every switch knows the topology to figure out how to do that
  When switch 1 receives the connection request, in addition to sending it on to switch 2, it creates a new entry in its VC table for this new connection
    The entry is exactly the same shown in the previous table
    Switch 1 picks the value 5 for this connection

## Slide 29: Switching and Forwarding
How does the signalling work (contd.)
  When switch 2 receives the setup message, it performs the similar process and it picks the value 11 as the incoming VCI
  Similarly switch 3 picks 7 as the value for its incoming VCI
    Each switch can pick any number it likes, as long as that number is not currently in use for some other connection on that port of that switch
  Finally the setup message arrives at host B.
  Assuming that B is healthy and willing to accept a connection from host A, it allocates an incoming VCI value, in this case 4.
    This VCI value can be used by B to identify all packets coming from A

## Slide 30: Switching and Forwarding
Now to complete the connection, everyone needs to be told what their downstream neighbor is using as the VCI for this connection
  Host B sends an acknowledgement of the connection setup to switch 3 and includes in that message the VCI value that it chose (4)
  Switch 3 completes the VC table entry for this connection and sends the acknowledgement on to switch 2 specifying the VCI of 7
  Switch 2 completes the VC table entry for this connection and sends acknowledgement on to switch 1 specifying the VCI of 11
  Finally switch 1 passes the acknowledgement on to host A telling it to use the VCI value of 5 for this connection

## Slide 31: Switching and Forwarding
When host A no longer wants to send data to host B, it tears down the connection by sending a teardown message to switch 1
The switch 1 removes the relevant entry from its table and forwards the message on to the other switches in the path which similarly delete the appropriate table entries
At this point, if host A were to send a packet with a VCI of 5 to switch 1, it would be dropped as if the connection had never existed

## Slide 32: Switching and Forwarding
Characteristics of VC
  Since host A has to wait for the connection request to reach the far side of the network and return before it can send its first data packet, there is at least one RTT of delay before data is sent
  While the connection request contains the full address for host B (which might be quite large, being a global identifier on the network), each data packet contains only a small identifier, which is only unique on one link.
    Thus the per-packet overhead caused by the header is reduced relative to the datagram model
  If a switch or a link in a connection fails, the connection is broken and a new one will need to be established.
    Also the old one needs to be torn down to free up table storage space in the switches
  The issue of how a switch decides which link to forward the connection request on has similarities with the function of a routing algorithm

## Slide 33: Switching and Forwarding
Good Properties of VC
  By the time the host gets the go-ahead to send data, it knows quite a lot about the network-
    For example, that there is really a route to the receiver and that the receiver is willing to receive data
  It is also possible to allocate resources to the virtual circuit at the time it is established

## Slide 34: Switching and Forwarding
For example, an X.25 network – a packet-switched network that uses the connection-oriented model – employs the following three-part strategy
  Buffers are allocated to each virtual circuit when the circuit is initialized
  The sliding window protocol is run between each pair of nodes along the virtual circuit, and this protocol is augmented with the flow control to keep the sending node from overrunning the buffers allocated at the receiving node
  The circuit is rejected by a given node if not enough buffers are available at that node when the connection request message is processed

## Slide 35: Switching and Forwarding
Comparison with the Datagram Model
  Datagram network has no connection establishment phase and each switch processes each packet independently
  Each arriving packet competes with all other packets for buffer space
  If there are no buffers, the incoming packet must be dropped
In VC, we could imagine providing each circuit with a different quality of service (QoS)
  The network gives the user some kind of performance related guarantee
    Switches set aside the resources they need to meet this guarantee
      For example, a percentage of each outgoing link’s bandwidth
      Delay tolerance on each switch
Most popular examples of VC technologies are Frame Relay and ATM
  One of the applications of Frame Relay is the construction of VPN

## Slide 36: ATM
ATM (Asynchronous Transfer Mode)
  Connection-oriented packet-switched network
  Packets are called cells
    5 byte header + 48 byte payload
  Fixed length packets are easier to switch in hardware
    Simpler to design
    Enables parallelism

## Slide 37: ATM
User – Network Interface (UNI)
  Host-to-switch format
  GFC: Generic Flow Control
  VPI: Virtual Path Identifier
  VCI: Virtual Circuit Identifier
  Type: management, congestion control
  CLP: Cell Loss Priority
  HEC: Header Error Check (CRC-8)
Network – Network Interface (NNI)
  Switch-to-switch format
  GFC becomes part of VPI field
ATM Cell Format

## Slide 38: Source Routing
All the information about network topology that is required to switch a packet across the network is provided by the source host

## Slide 39: Source Routing
Other approaches in source routing
Three ways to handle headers for source routing
  a) Rotation
  b) Stripping
  c) Pointer
The labels are read right to left

## Slide 40: Bridges and LAN Switches

## Slide 41: Bridges and LAN Switches
Class of switches that is used to forward packets between shared-media LANs such as Ethernets
  Known as LAN switches
  Referred to as Bridges
Suppose you have a pair of Ethernets that you want to interconnect
  One approach is put a repeater in between them
    It might exceed the physical limitation of the Ethernet
      No more than four repeaters between any pair of hosts
      No more than a total of 2500m in length is allowed

## Slide 42: Bridges and LAN Switches
  An alternative would be to put a node between the two Ethernets and have the node forward frames from one Ethernet to the other
    This node is called a bridge
    A collection of LANs connected by one or more bridges is usually said to form an extended LAN

## Slide 43: Bridges and LAN Switches
Simplest Strategy for Bridges
  Accept LAN frames on their inputs and forward them out to all other outputs
  Used by early bridges
Learning Bridges
  Observe that there is no need to forward all the frames that a bridge receive

## Slide 44: Bridges and LAN Switches
Consider the following figure
  When a frame from host A that is addressed to host B arrives on port 1 there is no need for the bridge to forward the frame out over port 2
  How does a bridge come to learn on which port the various hosts reside?

## Slide 45: Bridges and LAN Switches
Solution
  Download a table into the bridge
Who does the download
  Human
    Too much work for maintenance
Host | Port
A | 1
B | 1
C | 1
X | 2
Y | 2
Z | 2

## Slide 46: Bridges and LAN Switches
Can the bridge learn this information by itself?
  Yes
How
  Each bridge inspects the source address in all the frames it receives
  Record the information at the bridge and build the table
  Entries are added over time
  A timeout is associated with each entry
  The bridge discards the entry after a specified period of time
    To protect against the situation in which a host is moved from one network to another

## Slide 47: Bridges and LAN Switches
If the bridge receives a frame that is addressed to host not currently in the table
  Forward the frame out on all other ports
Strategy works fine if the extended LAN does not have a loop in it
Why?
  Frames potentially loop through the extended LAN forever
  Bridges B1, B4 and B6 form a loop

## Slide 48: Bridges and LAN Switches
How does an extended LAN come to have a loop in it?
  Network is managed by more than one administrator
    For example, it spans multiple departments in an organization
    It is possible that no single person knows the entire configuration of the network
      A bridge that closes a loop might be added without any one knowing
  Loops are built into the network to provide redundancy in case of failures
Solution
  Distributed Spanning Tree Algorithm

## Slide 49: Spanning Tree Algorithm
Think of the extended LAN as being represented by a graph that possibly has loops (cycles)
A spanning tree is a sub-graph of this graph that covers all the vertices but contains no cycles
  Spanning tree keeps all the vertices of the original graph but throws out some of the edges
  Example of (a) a cyclic graph; (b) a corresponding spanning tree.

## Slide 50: Spanning Tree Algorithm
Developed by Radia Perlman at Digital
  a protocol used by a set of bridges to agree upon a spanning tree for a particular extended LAN
  IEEE 802.1 specification for LAN bridges is based on this algorithm
  Each bridge decides the ports over which it is and is not willing to forward frames
    In a sense, it is by removing ports from the topology that the extended LAN is reduced to an acyclic tree
    It is even possible that an entire bridge will not participate in forwarding frames

## Slide 51: Spanning Tree Algorithm
Algorithm is dynamic
  The bridges are always prepared to reconfigure themselves into a new spanning tree if some bridges fail
Main idea
  Each bridge selects the ports over which they will forward the frames

## Slide 52: Spanning Tree Algorithm
Algorithm selects ports as follows:
  Each bridge has a unique identifier
    B1, B2, B3,…and so on.
  Elect the bridge with the smallest id as the root of the spanning tree
  The root bridge always forwards frames out over all of its ports
  Each bridge computes the shortest path to the root and notes which of its ports is on this path
    This port is selected as the bridge’s preferred path to the root
  Finally, all the bridges connected to a given LAN elect a single designated bridge that will be responsible for forwarding frames toward the root bridge

## Slide 53: Spanning Tree Algorithm
Each LAN’s designated bridge is the one that is closest to the root
If two or more bridges are equally close to the root,
  Then select bridge with the smallest id
Each bridge is connected to more than one LAN
  So it participates in the election of a designated bridge for each LAN it is connected to.
  Each bridge decides if it is the designated bridge relative to each of its ports
  The bridge forwards frames over those ports for which it is the designated bridge

## Slide 54: Spanning Tree Algorithm
B1 is the root bridge
B3 and B5 are connected to LAN A, but B5 is the designated bridge
B5 and B7 are connected to LAN B, but B5 is the designated bridge

## Slide 55: Spanning Tree Algorithm
Initially each bridge thinks it is the root, so it sends a configuration message on each of its ports identifying itself as the root and giving a distance to the root of 0
Upon receiving a configuration message over a particular port, the bridge checks to see if the new message is better than the current best configuration message recorded for that port
The new configuration is better than the currently recorded information if
  It identifies a root with a smaller id or
  It identifies a root with an equal id but with a shorter distance or
  The root id and distance are equal, but the sending bridge has a smaller id

## Slide 56: Spanning Tree Algorithm
If the new message is better than the currently recorded one,
  The bridge discards the old information and saves the new information
  It first adds 1 to the distance-to-root field
When a bridge receives a configuration message indicating that it is not the root bridge (that is, a message from a bridge with smaller id)
  The bridge stops generating configuration messages on its own
  Only forwards configuration messages from other bridges after 1 adding to the distance field

## Slide 57: Spanning Tree Algorithm
When a bridge receives a configuration message that indicates it is not the designated bridge for that port
  => a message from a bridge that is closer to the root or equally far from the root but with a smaller id
    The bridge stops sending configuration messages over that port
When the system stabilizes,
  Only the root bridge is still generating configuration messages.
  Other bridges are forwarding these messages only over ports for which they are the designated bridge

## Slide 58: Spanning Tree Algorithm
Consider the situation when the power had just been restored to the building housing the following network
All bridges would start off by claiming to be the root

## Slide 59: Spanning Tree Algorithm
Denote a configuration message from node X in which it claims to be distance d from the root node Y as (Y, d, X)
Consider the activity at node B3

## Slide 60: Spanning Tree Algorithm
B3 receives (B2, 0, B2)
Since 2 < 3, B3 accepts B2 as root
B3 adds 1 to the distance advertised by B2 and sends (B2, 1, B3) to B5
Meanwhile B2 accepts B1 as root because it has the lower id and it sends (B1, 1, B2) toward B3
B5 accepts B1 as root and sends (B1, 1, B5) to B3
B3 accepts B1 as root and it notes that both B2 and B5 are closer to the root than it is.
  Thus B3 stops forwarding messages on both its interfaces
  This leaves B3 with both ports not selected

## Slide 61: Spanning Tree Algorithm
Even after the system has stabilized, the root bridge continues to send configuration messages periodically
  Other bridges continue to forward these messages
When a bridge fails, the downstream bridges will not receive the configuration messages
After waiting a specified period of time, they will once again claim to be the root and the algorithm starts again
Note
  Although the algorithm is able to reconfigure the spanning tree whenever a bridge fails, it is not able to forward frames over alternative paths for the sake of routing around a congested bridge

## Slide 62: Broadcast and Multicast
Forwarding all broadcast/multicast frames
  Current practice
Learn when no group members downstream
Accomplished by having each member of group G and send a frame to bridge multicast address with G in source field

## Slide 63: Limitation of Bridges
Do not scale
  Spanning tree algorithm does not scale
  Broadcast does not scale
Do not accommodate heterogeneity

## Slide 64: Cell Switching (ATM)

## Slide 65: Cell Switching (ATM)
1980s and early 1990s; embraced by telephone industry
Used in both WAN and LAN setting
Specified by ATM forum
Connection-oriented (virtual circuit switching), packet-switched network
  Signalling (Connection setup) protocol: Q.2931
Packets are called cells: 5-byte header + 48-byte payload
Commonly transmitted over SONET
  Other physical layers possible

## Slide 66: Variable Vs Fixed-Length Packets
No optimal length => variable-length packet
  If small: high header-to-data overhead
  If large: low utilization for small messages
Fixed-Length Easier to Switch in Hardware
  Simpler to implement
  Enables parallelism (since length is known and fixed)

## Slide 67: Big Vs Small Packets
Small Improves Queue behavior
  finer-grained preemption point for scheduling link
    maximum packet = 4KB
    Link speed = 100Mbps
    transmission time = 4096 x 8/100 = 327.68us
    High priority packet may sit in the queue 327.68us
    In contrast, 53 x 8/100 = 4.24us for ATM
  near cut-through behavior
    two 4KB packets arrive at same time
    link idle for 327.68us while both arrive
      Because the switch must wait to receive the whole first packet before starting transmitting it
    at end of 327.68us, still have 8KB to transmit
    in contrast, can transmit first cell after 4.24us
    at end of 327.68us, just over 4KB left in queue

## Slide 68: Big Vs Small Packets
Small Reduces Latency (for voice)
  voice digitally encoded at 64KBps (8-bit samples at 8KHz)
  need full cell’s worth of samples before sending cell
  example: 1000-byte cells implies 125ms per cell (too long)
  smaller latency implies no need for echo cancellers (since a very small latency feels like “0 latency”)
ATM Compromise: 48 bytes
  US: would like it to be 64 bytes (has echo canceller, thus can afford large packets to reduce header-to-payload ratio)
  Europe: advocates 32 bytes (no echo canceller, thus need small packet)
  Compromise: 48 = (32+64)/2

## Slide 69: Cell Format
User-Network Interface (UNI): host-to-switch format
  GFC: Generic Flow Control (still being defined)
  VPI: Virtual Path Identifier
  VCI: Virtual Circuit Identifier
  Type: management, congestion control, AAL5 (later)
  CLP: Cell Loss Priority
  HEC: Header Error Check (CRC-8)
Network-Network Interface (NNI): switch-to-switch format
  GFC becomes part of VPI field

## Slide 70: Segmentation and Reassembly
Accomplished by ATM Adaptation Layer (AAL)
Two sub layers:
  Higher layer: Convergence Sub layer (CS)
    responsible for packaging the higher layer PDU (protocol data unit) with additional information required for the adaptation necessary for specific service types (e.g., bit rate, connection-oriented or connectionless)
  Lower layer: Segmentation and Reassembly (SAR)

## Slide 71: Different Types of AALs
AAL 1 and 2 designed for applications that need guaranteed rate (e.g., voice, video)
AAL 3/4 designed for data packet
AAL 5 is an alternative standard for data packet

## Slide 72: AAL 3/4
Convergence Sub layer Protocol Data Unit (CS-PDU)
  CPI: common part indicator (version field); not used yet
  Btag/Etag: beginning and ending tag (deal with cell corruption)
  BAsize: hint on amount of buffer space to allocate
  Length: size of whole PDU

## Slide 73: SAR: Cell Format --- payload
Type
  BOM: beginning of message
  COM: continuation of message
  EOM end of message
SEQ: sequence number
MID: multiplexing identifier
Length: number of bytes of payload (from CS-PDU) in this cell; in bytes

## Slide 74: Encapsulation & segmentation for AAL3/4

## Slide 75: AAL5
Simplifies the format of AAL ¾
CS-PDU Format
  Pad, so trailer always falls at end of ATM cell
  Len: size of PDU (data only); in bytes
  CRC-32 (detects missing or misordered cells)
SAR: Cell Format --- payload
  end-of-PDU bit in Type field of ATM header
  Compared with AAL 3/4 , AAL 5 does not provide an additional level of multiplexing onto one virtual circuit (which was achieved via MID in AAL¾)

## Slide 76: Encapsulation & segmentation for AAL 5

## Slide 77: Virtual path
Two-level hierarchy of virtual connections
  Virtual path (VP)
  Virtual circuit (VC)
Switches in public network only maintains state about VPs, which is much fewer than the number of VCs
  Thus, improves systems scalability

## Slide 78: Cell Switching
Implementation and Performance

## Slide 79: A workstation used as a packet switch
Flexible in trying out different routing/switching strategies
  Experimental systems
(-) high switching overhead, and thus potentially low throughput

## Slide 80: A 4×4 switch
Input ports: switching logic control (e.g., which output ports to forward packets); usually do not buffer packets
Switch fabric: forward packets from input ports to output ports; may have internal buffer space
Output ports: buffering

## Slide 81: Switch Fabrics
Shared Bus
  This type of switches used in conventional workstation
  Bandwidth determines the throughput of the switch
Shared Memory
  Packets are written into a memory location by an input port and then read from memory by the output ports
  Memory bandwidth determines switch throughput
Crossbar:
  Switch is a matrix of pathways that can be configured to connect any input port to any output port

## Slide 82: Crossbar Switch
A 4 x 4 Crossbar Switch

## Slide 83: Switch Fabrics
Self-routing:
  Rely on some information in the packet header to direct each packet to its correct output

## Slide 84: Switch fabrics (contd.)
Self-routing header is applied to a packet at input to enable the fabric to send the packet to the correct output, where it is removed
Packet arrives at the input port
Input port attaches self-routing header to direct packet to correct output
Self-routing header is removed at output port before packet leaves switch

## Slide 85: Switch fabrics (contd.)
Banyan Network: switch elements in 1st column looks at the most significant bit of output port number: 0 -> route packet to the top; 1 -> route to bottom …
Batcher-Banyan Switch design: Batcher network first sorts packets (for parallel tx.), then the packets are sent to Banyan network

## Slide 86: Reference
Chapter – 3: Computer Networks A Systems Approach by Larry L. Peterson and Bruce S. Davie, 4Th Edition, Morgan Kaufmann Publications.