## Slide 1: internetworking

## Slide 2: Outline
Simple Internetworking (IP)
Routing
Multicast

## Slide 3: Simple Internetworking (IP)
What is an Internetwork

## Slide 4: What is Internetworking
An arbitrary collection of networks interconnected to provide some sort of host – host packet delivery service
A simple internetwork where H represents hosts and R represents routers

## Slide 5: What is IP
IP stands for Internet Protocol
Key tool used today to build scalable, heterogeneous internetworks
It runs on all the nodes in a collection of networks and defines the infrastructure that allows these nodes and networks to function as a single logical internetwork
  A simple internetwork showing the protocol layers

## Slide 6: IP Service Model
Packet Delivery Model
  Connectionless model for data delivery
  Best-effort delivery (unreliable service)
    Packets are lost
    Packets are delivered out of order
    Duplicate copies of a packet are delivered
    Packets can be delayed for a long time
Global Addressing Scheme
  Provides a way to identify all hosts in the network

## Slide 7: Packet Format (IPv4)
Version (4)
Hlen(4): number of 32-bit words in header
TOS(8): Type of service (not widely used)
Length(16): number of bytes in this datagram
Idnet(16): used by fragmentation
Flags/Offset(16): used by fragmentation
TTL(8): number of hops this datagram has traveled
Protocol(8): demux key (TCP=6, UDP=17)
Checksum(16): of the header only
DestAddr & SrcAddr (32)

## Slide 8: IP Fragmentation and Reassembly
Each network has some MTU (Maximum Transmission Unit)
  Ethernet (1500 bytes), FDDI (4500 bytes)
Strategy
  Fragmentation occurs in a router when it receives a datagram that it wants to forward over a network which has (MTU < datagram)
  Reassembly is done at the receiving host
  All the fragments carry the same identifier in the Ident field
  Fragments are self-contained datagrams
  IP does not recover from missing fragments

## Slide 9: IP Fragmentation and Reassembly
  IP datagrams traversing the sequence of physical networks

## Slide 10: IP Fragmentation and Reassembly
Header fields used in IP fragmentation. (a) Unfragmented packet; (b) fragmented packets.

## Slide 11: Global Addresses
Properties
  Globally unique
  Hierarchical: network + host
  4 Billion IP address, half are A type, ¼ is B type, and 1/8 is the C type
Format
Dot notation
  10.3.2.4
  128.96.33.81
  192.12.69.77

## Slide 12: IP Datagram Forwarding
Strategy
  Every datagram contains destination’s address
  If directly connected to destination network, then forward to host
  If not directly connected to destination network, then forward to some router
  Forwarding table maps network number into next hop
  Each host has a default router
  Each router maintains a forwarding table
Example (router R2)
NetworkNum | NextHop
1 | R1
2 | Interface 1
3 | Interface 0
4 | R3

## Slide 13: IP Datagram Forwarding - Algorithm
if (NetworkNum of destination = NetworkNum of one of my interfaces) then
deliver packet to destination over that interface
else
if (NetworkNum of destination is in my forwarding table) then
deliver packet to NextHop router
else
deliver packet to default router
For a host with only one interface and only a default router in its forwarding table, this simplifies to
if (NetworkNum of destination = my NetworkNum)then
deliver packet to destination directly
else
deliver packet to default router

## Slide 14: Subnetting
Add another level to address/routing hierarchy: subnet
Subnet masks define variable partition of host part of class A and B addresses
Subnets visible only within site

## Slide 15: Subnetting
Forwarding Table at Router R1

## Slide 16: Subnetting
Forwarding Algorithm
D = destination IP address
for each entry < SubnetNum, SubnetMask, NextHop>
  D1 = SubnetMask & D
  if D1 = SubnetNum
    if NextHop is an interface
    deliver datagram directly to destination
    else
    deliver datagram to NextHop (a router)

## Slide 17: Subnetting
Would use a default router if nothing matches
Not necessary for all ones in subnet mask to be contiguous
Can put multiple subnets on one physical network
Subnets not visible from the rest of the internet

## Slide 18: Classless Addressing
Classless Inter-Domain Routing
  A technique that addresses two scaling concerns in the Internet
    The growth of backbone routing table as more and more network numbers need to be stored in them
    Potential exhaustion of the 32-bit address space
  Address assignment efficiency
    Arises because of the IP address structure with class A, B and C addresses
    Forces us to hand out network address space in fixed-size chunks of three very different sizes
      A network with two hosts needs a class C address
        Address assignment efficiency = 2/255 = 0.78
      A network with 256 hosts needs a class B address
        Address assignment efficiency = 256/65535 = 0.39

## Slide 19: Classless Addressing
Exhaustion of IP address space center on exhaustion of the class B network numbers
Solution
  Say “NO” to any autonomous system(AS) that requests a class B address unless they can show a need for something close to 64K addresses
  Instead give them an appropriate number of class C addresses
  For any AS with at least 256 hosts, we can guarantee an address space utilization of at least 50%

## Slide 20: Classless Addressing
Problem with this solution
  Excessive storage requirement at the routers
If a single AS has, say 16 class C network numbers assigned to it
  Every Internet backbone router needs 16 entries in its routing tables for that AS
  This is true, even if the path to every one of these networks is the same
If we had assigned a class B address to the AS
  The same routing information can be stored in one entry
  Efficiency = 16 x (255/65,536) = 6.2%

## Slide 21: Classless Addressing
CIDR tries to balance the desire to minimize the number of routes that a router needs to know against the need to hand out addresses efficiently
CIDR uses aggregate routes
  Uses a single entry in the forwarding table to tell the router how to reach a lot of different networks
  Breaks the rigid boundaries between address classes

## Slide 22: Classless Addressing
Consider an AS with 16 class C network numbers.
Instead of handing out 16 addresses at random, hand out a block of contiguous class C addresses
Suppose we assign the class C network numbers from 192.4.16 through 192.4.31
Observe that top 20 bits of all the addresses in this range are the same (11000000 00000100 0001)
  We have created a 20-bit network number (which is in between class B network number and class C number)
Requires to hand out blocks of class C addresses that share a common prefix

## Slide 23: Classless Addressing
Requires to hand out blocks of class C addresses that share a common prefix
The convention is to place a /X after the prefix where X is the prefix length in bits
For example, the 20-bit prefix for all the networks 192.4.16 through 192.4.31 is represented as 192.4.16/20
By contrast, if we wanted to represent a single class C network number, which is 24 bits long, we would write it 192.4.16/24

## Slide 24: Classless Addressing
How do the routing protocols handle this classless addresses
  It must understand that the network number may be of any length
Represent network number with a single pair
    <length, value>
All routers must understand CIDR addressing

## Slide 25: Classless Addressing
Route aggregation with CIDR

## Slide 26: IP Forwarding Revisited
IP forwarding mechanism assumes that it can find the network number in a packet and then look up that number in the forwarding table
We need to change this assumption in case of CIDR
CIDR means that prefixes may be of any length, from 2 to 32 bits

## Slide 27: IP Forwarding Revisited
It is also possible to have prefixes in the forwarding tables that overlap
  Some addresses may match more than one prefix
For example, we might find both 171.69 (a 16 bit prefix) and 171.69.10 (a 24 bit prefix) in the forwarding table of a single router
A packet destined to 171.69.10.5 clearly matches both prefixes.
  The rule is based on the principle of “longest match”
    171.69.10 in this case
A packet destined to 171.69.20.5 would match 171.69 and not 171.69.10

## Slide 28: Address Translation Protocol (ARP)
Map IP addresses into physical addresses
  destination host
  next hop router
Techniques
  encode physical address in host part of IP address
  table-based
ARP (Address Resolution Protocol)
  table of IP to physical address bindings
  broadcast request if IP address not in table
  target machine responds with its physical address
  table entries are discarded if not refreshed

## Slide 29: ARP Packet Format
HardwareType: type of physical network (e.g., Ethernet)
ProtocolType: type of higher layer protocol (e.g., IP)
HLEN & PLEN: length of physical and protocol addresses
Operation: request or response
Source/Target Physical/Protocol addresses

## Slide 30: Host Configuration
Ethernet addresses are configured into network by manufacturer and they are unique
IP addresses must be unique on a given internetwork but also must reflect the structure of the internetwork
Most host Operating systems provide a way to manually configure the IP information for the host
Drawbacks of manual configuration
  A lot of work to configure all the hosts in a large network
  Configuration process is error-prune
Automated configuration processes is required

## Slide 31: Dynamic Host Configuration Protocol (DHCP)
DHCP server is responsible for providing configuration information to hosts
There is at least one DHCP server for an administrative domain
DHCP server maintains a pool of available addresses

## Slide 32: DHCP
Newly booted or attached host sends DHCPDISCOVER message to a special IP address (255.255.255.255)
DHCP relay agent unicasts the message to DHCP server and waits for the response

## Slide 33: Internet Control Message Protocol (ICMP)
Defines a collection of error messages that are sent back to the source host whenever a router or host is unable to process an IP datagram successfully
  Destination host unreachable due to link/node failure
  Reassembly process failed
  TTL had reached 0 (so datagram don’t cycle forever)
  IP header checksum failed
ICMP – Redirect
  From router to a source host
  With a better route information

## Slide 34: Routing
Forwarding Versus Routing
  Forwarding
    To select an output port based on destination address and routing table
  Routing
    Process by which routing table is built

## Slide 35: Routing – Forwarding Table Vs Routing Table
Forwarding Table
  Used when a packet is being forwarded and so must contain enough information to accomplish the forwarding function
  A row in the forwarding table contains the mapping from a network number to an outgoing interface and some MAC information, such as Ethernet address of the next hop
Routing Table
  Built by the routing algorithm as a precursor to build the forwarding table
  Generally contains mapping from network numbers to next hops

## Slide 36: Routing
  Example rows from (a) routing and (b) forwarding tables

## Slide 37: Routing
Network as a Graph
The basic problem of routing is to find the lowest-cost path between any two nodes
  Where the cost of a path equals the sum of the costs of all the edges that make up the path

## Slide 38: Routing
For a simple network, we can calculate all shortest paths and load them into some nonvolatile storage on each node
Such a static approach has several shortcomings
  It does not deal with node or link failures
  It does not consider the addition of new nodes or links
  It implies that edge costs cannot change
Why is the solution?
  Need a distributed and dynamic protocol
  Two main classes of protocols
    Distance Vector
    Link State

## Slide 39: Distance Vector
Each node constructs a one dimensional array (a vector) containing the “distances” (costs) to all other nodes and distributes that vector to its immediate neighbors
Starting assumption is that each node knows the cost of the link to each of its directly connected neighbors

## Slide 40: Distance Vector
Initial distances stored at each node (global view)

## Slide 41: Distance Vector
Initial routing table at node A

## Slide 42: Distance Vector
Final routing table at node A

## Slide 43: Distance Vector
Final distances stored at each node (global view)

## Slide 44: Distance Vector
The distance vector routing algorithm is sometimes called as Bellman-Ford algorithm
Every T seconds each router sends its table to its neighbor each router then updates its table based on the new information
Problems include fast response to good new and slow response to bad news. Also too many messages to update

## Slide 45: Distance Vector
When a node detects a link failure
  F detects that link to G has failed
  F sets distance to G to infinity and sends update to A
  A sets distance to G to infinity since it uses F to reach G
  A receives periodic update from C with 2-hop path to G
  A sets distance to G to 3 and sends update to F
  F decides it can reach G in 4 hops via A

## Slide 46: Distance Vector
Slightly different circumstances can prevent the network from stabilizing
  Suppose the link from A to E goes down
  In the next round of updates, A advertises a distance of infinity to E, but B and C advertise a distance of 2 to E
  Depending on the exact timing of events, the following might happen
    Node B, upon hearing that E can be reached in 2 hops from C, concludes that it can reach E in 3 hops and advertises this to A
    Node A concludes that it can reach E in 4 hops and advertises this to C
    Node C concludes that it can reach E in 5 hops; and so on
    This cycle stops only when the distances reach some number that is large enough to be considered infinite
      Count – to – infinity problem

## Slide 47: Count-to-infinity Problem
Use some relatively small number as an approximation of infinity
For example, the maximum number of hops to get across a certain network is never going to be more than 16
One technique to improve the time to stabilize routing is called split horizon
  When a node sends a routing update to its neighbors, it does not send those routes it learned from each neighbor back to that neighbor
  For example, if B has the route (E, 2, A) in its table, then it knows it must have learned this route from A, and so whenever B sends a routing update to A, it does not include the route (E, 2) in that update

## Slide 48: Count – to – infinity Problem
In a stronger version of split horizon, called split horizon with poison reverse
  B actually sends that back route to A, but it puts negative information in the route to ensure that A will not eventually use B to get to E
  For example, B sends the route (E, ) to A

## Slide 49: Routing Information Protocol (RIP)
RIPv2 Packet Format
  Example Network running RIP

## Slide 50: Link State Routing
Strategy: Send to all nodes (not just neighbors) information about directly connected links (not entire routing table)
Link State Packet (LSP)
  Id of the node that created the LSP
  Cost of link to each directly connected neighbor
  Sequence number (SEQNO)
  Time-to-live (TTL) for this packet
Reliable Flooding
  Store most recent LSP from each node
  Forward LSP to all nodes but one that send it
  Generate new LSP periodically; increment SEQNO
  Start SEQNO at 0 when reboot
  Decrement TTL of each stored LSP; discard when TTL = 0

## Slide 51: Link State
Reliable Flooding
Flooding of link-state packets. (a) LSP arrives at node X; (b) X floods LSP to A and C; (c) A and C flood LSP to B (but not X); (d) flooding is complete

## Slide 52: Shortest Path Routing
Dijkstra’s Algorithm - Assume non-negative link weights
  N: set of nodes in the graph
  l((i, j): the non-negative cost associated with the edge between nodes i, j N and l(i, j) =  if no edge connects i and j
  Let s N be the starting node which executes the algorithm to find shortest paths to all other nodes in N
  Two variables used by the algorithm
    M: set of nodes incorporated so far by the algorithm
    C(n) : the cost of the path from s to each node n
    The algorithm
      M = {s}
      For each n in N – {s}
        C(n) = l(s, n)
      while ( N  M)
        M = M  {w} such that C(w) is the minimum
        for all w in (N-M)
        For each n in (N-M)
        C(n) = MIN (C(n), C(w) + l(w, n))

## Slide 53: Shortest Path Routing
In practice, each switch computes its routing table directly from the LSP’s it has collected using a realization of Dijkstra’s algorithm called the forward search algorithm
Specifically each switch maintains two lists, known as Tentative and Confirmed
Each of these lists contains a set of entries of the form (Destination, Cost, NextHop)

## Slide 54: Shortest Path Routing
The algorithm
  Initialize the Confirmed list with an entry for myself; this entry has a cost of 0
  For the node just added to the Confirmed list in the previous step, call it node Next, select its LSP
  For each neighbor (Neighbor) of Next, calculate the cost (Cost) to reach this Neighbor as the sum of the cost from myself to Next and from Next to Neighbor
    If Neighbor is currently on neither the Confirmed nor the Tentative list, then add (Neighbor, Cost, Nexthop) to the Tentative list, where Nexthop is the direction I go to reach Next
    If Neighbor is currently on the Tentative list, and the Cost is less than the currently listed cost for the Neighbor, then replace the current entry with (Neighbor, Cost, Nexthop) where Nexthop is the direction I go to reach Next
  If the Tentative list is empty, stop. Otherwise, pick the entry from the Tentative list with the lowest cost, move it to the Confirmed list, and return to Step 2.

## Slide 55: Shortest Path Routing

## Slide 56: Open Shortest Path First (OSPF)
OSPF Link State Advertisement
OSPF Header Format

## Slide 57: IPv6

## Slide 58: Major Features
128 – bit addresses
Multicast
Real-time service
Authentication and security
Auto-configuration
End-to-end fragmentation
Enhanced routing functionality, including support for mobile hosts

## Slide 59: IPv6 Addresses
Classless addressing/routing (similar to CIDR)
Notation: x:x:x:x: x:x:x:x (x = 16-bit hex number)
  Contiguous 0s are compressed: 47CD::A456:0124
  IPv6 compatible IPv4 address: 128.42.1.87
Address assignment
  Provider-based
  Geographic

## Slide 60: IPv6 Header
40-byte “base” header
Extension headers (fixed order, mostly fixed length)
  Fragmentation
  Source routing
  Authentication and security
  Other options

## Slide 61: Internet Multicast

## Slide 62: Multicast
One-to-many
  Radio station broadcast
  Transmitting news, stock-price
  Software updates to multiple hosts
Many-to-many
  Multimedia teleconferencing
  Online multi-player games
  Distributed simulations

## Slide 63: Multicast
Without support for multicast
  A source needs to send a separate packet with the identical data to each member of the group
    This redundancy consumes more bandwidth
    Redundant traffic is not evenly distributed, concentrated near the sending host
  Source needs to keep track of the IP address of each member in the group
    Group may be dynamic
To support many-to-many and one-to-many IP provides as IP-level multicast

## Slide 64: Multicast
Basic IP multicast model is many-to-many based on multicast groups
  Each group has its own IP multicast address
  Hosts that the members of a group receive copies of any packets sent to that group’s multicast address
  A host can be in multiple groups
  A host can join and leave groups

## Slide 65: Multicast
Using IP multicast to send the identical packet to each member of the group
  A host sends a single copy of the packet addressed to the group’s multicast address
  The sending host does not need to know the individual unicast IP address of each member
  Sending host does not send multiple copies of the packet

## Slide 66: Multicast
IP’s original many-to-many multicast has been supplemented with support for a form of one-to-many multicast
One-to-many multicast
  Source specific multicast (SSM)
  A receiving host specifies both a multicast group and a specific sending host
Many-to-many model
  Any source multicast (ASM)

## Slide 67: Multicast
A host signals its desire to join or leave a multicast group by communicating with its local router using a special protocol
  In IPv4, the protocol is Internet Group Management Protocol (IGMP)
  In IPv6, the protocol is Multicast Listener Discovery (MLD)
The router has the responsibility for making multicast behave correctly with regard to the host

## Slide 68: Multicast Routing
A router’s unicast forwarding tables indicate for any IP address, which link to use to forward the unicast packet
To support multicast, a router must additionally have multicast forwarding tables that indicate, based on multicast address, which links to use to forward the multicast packet
Unicast forwarding tables collectively specify a set of paths
Multicast forwarding tables collectively specify a set of trees
  Multicast distribution trees

## Slide 69: Multicast Routing
To support source specific multicast, the multicast forwarding tables must indicate which links to use based on the combination of multicast address and the unicast IP address of the source
Multicast routing is the process by which multicast distribution trees are determined

## Slide 70: Distance-Vector Multicast
Each router already knows that shortest path to source S goes through router N.
When receive multicast packet from S, forward on all outgoing links (except the one on which the packet arrived), iff packet arrived from N.
Eliminate duplicate broadcast packets by only letting
  “parent” for LAN (relative to S) forward
    shortest path to S (learn via distance vector)
    smallest address to break ties

## Slide 71: Distance Vector Multicast
Reverse Path Broadcast (RPB)
Goal: Prune networks that have no hosts in group G
Step 1: Determine of LAN is a leaf with no members in G
  leaf if parent is only router on the LAN
  determine if any hosts are members of G using IGMP
Step 2: Propagate “no members of G here” information
  augment <Destination, Cost> update sent to neighbors with set of groups for which this network is interested in receiving multicast packets.
  only happens when multicast address becomes active.

## Slide 72: Protocol Independent Multicast (PIM)
Shared Tree
Source specific tree

## Slide 73: Protocol Independent Multicast (PIM)
Delivery of a packet along a shared tree. R1 tunnels the packet to the RP, which forwards it along the shared tree to R4 and R5.

## Slide 74: Inter – domain Multicast
Multicast Source Discovery Protocol (MSDP)

## Slide 75: Routing for Mobile Hosts
Mobile IP
  Home Agent
    Router located on the home network of the mobile hosts
  Home Address
    The permanent IP address of the mobile host
    Has a network number equal to that of the home network and thus of the home agent
  Foreign Agent
    Router located on a network to which the mobile node attaches itself when it is away from its home network

## Slide 76: Routing for Mobile Hosts

## Slide 77: Routing for Mobile Hosts
Problem of delivering a packet to the mobile node
  How does the home agent intercept a packet that is destined for the mobile node?
    Proxy ARP
  How does the home agent then deliver the packet to the foreign agent?
    IP tunnel
    Care – of – address
  How does the foreign agent deliver the packet to the mobile node?

## Slide 78: Routing for Mobile Hosts
Route optimization in Mobile IP
  The route from the sending node to mobile node can be significantly sub-optimal
  One extreme example
    The mobile node and the sending node are on the same network, but the home network for the mobile node is on the far side of the internet
      Triangle Routing Problem

## Slide 79: Routing for Mobile Hosts
Solution
  Let the sending node know the care-of-address of the mobile node. The sending node can create its own tunnel to the foreign agent
  Home agent sends binding update message
  The sending node creates an entry in the binding cache
  The binding cache may become out-of-date
    The mobile node moved to a different network
    Foreign agent sends a binding warning message

## Slide 80: Reference
Chapter – 4: Computer Networks A Systems Approach by Larry L. Peterson and Bruce S. Davie, 4Th Edition, Morgan Kaufmann Publications.